Series 2S00 – Three-Phase 400VAC

# Active Harmonic Filter Series

The TimesOne™ Active Harmonic Filter series lowers the electrical costs of operating commercial and industrial facilities and it’s equipment, with an investment payback, typically, less than two years.  The Active Harmonic Filter reduces energy costs by minimizing harmonics, and increasing Power Factor and correcting voltage imbalance.

- Energy Savings with 1- to 3-year ROI

- Power Factor Correction up to 100%

- Correct Voltage Imbalance for higher Motor Efficiency

- Reduce Operating Temperature of Electrical System

- Performance Guarantee by a System Energy Audit

- Reduce lost work in process

- Reduce Harmonic Distortion to ≤ 5% for the ITHD and VTHD

- Protect against Disruptive Transients

- Minimal Maintenance Required

- Increase Electrical System Capacity

- Accommodate Future Expansion

- Extended Warranty Program

# What is the Active Harmonic Filter?

An Active Harmonic Filter is an electronic power inverter using IGBT semiconductors with various control loops to increase Power Factor and reduce harmonics by injecting a dynamic cancellation signal into the power line.  Thereby reducing amperage, KVA, KVAR, circulating currents, harmonic resonance, line voltage imbalance and closed delta-winding losses.  The Active Harmonic Filter solution from Power Correction Systems improves the efficiency and operation of AC Motor Systems, AC Variable Frequency Drive (VFD) Systems and works well with virtually every Electrical and Electronic Device in your facility.  Conforms to IEEE 519-1996 and IEC 1000-2-2.

# Who needs the Active Harmonic Filter Solution?

You do, if you are operating with today’s sophisticated automation using VFDs DC Drives, SCRs, Process Controllers, computer-based Robotics, rectifier-based equipment or any other non-linear loads in commercial or industrial application.  Any facility, from the oldest to the newest, which incorporates non-linear process controls and VFDs In its operation, is a potential beneficiary of an Active Harmonic Filter solution.

You also need this solution, if you would like to reduce the costs of your electrical operation of your facility.  In the past, efficiency was increased by installing and using standard capacitors on power lines.  However, with the implementation of modern sophisticated automation, the increase in the amount of switching supplies and rectifier circuits now being used in manufacturing has caused efficiency to decrease.  These switching supplies and rectifier circuits create harmonics that can overheat capacitors.  Industry engineers and consultants agree that the application of standard capacitors to these systems is NOT always possible or feasible, and in some cases detrimental to the electrical systems.  A detrimental system resonance can occur and cause 100% over-voltage conditions when there are harmonics circulating.

Power Correction Systems offers advanced solutions to the problems of harmonics, Power Factor and voltage imbalance, the Active Harmonic Filter series provides economic savings and enhanced systems reliability due to Power Quality.  Installation of the Active Harmonic Filter is quick and easy, requiring no mechanical break to the power lines.

Typical Return Of Investment from 1 to 3 years.

# ECONOMIC BENEFITS:

- Lower Electric bills and KVA charges up to 30%

- Reduce peak energy demand charges

- Eliminate Power Factor penalties while improving electrical system efficiency

- Longer equipment life – less maintenance, repair and replacement cost of contactors, heaters, motors and transformers

- Improve safety – lower temperature of cables, generators, motors and transformers

- Decrease production losses and downtime of operations

- Increase power system equipment capacity for future expansion

LOSSES

### Typical Single-Phase Measurements of non-linear

### loads generating harmonics

(The same criteria apply to Three-Phase Systems)

Current Reduction Analysis

The signal injected by the Active Harmonic Filter reduces the RMS current drawn by this typical load from 13.1A RMS to 10.79A RMS.  While the peak current was reduced from 33.0A Peak to 15.83A Peak, a 52% reduction in the peak current demand.

Voltage Analysis

Voltage stabilization is another key feature of an Active Harmonic Filter solution.  Low and a fluctuating voltage supply can cause equipment malfunction and lost of in process work.  Note removal of the flat topping of the AC waveform and voltage correction to 118.7V RMS

# TECHNICAL BENEFITS:

- Improve Power Factor to almost 100% without an external de-tuned LC filter or de-rating the Active Harmonic Filter

- Reduce KVA, KVAR, KW and KWh by up to 30%, caused by low Power Factor and harmonics

- Reduce KVA demand caused by system voltage imbalance  (1% VIMBALANCE up to 6% IIMBALANCE)

- Eliminate over-heated neutrals

- Wide range of ILOAD operation

- No recalibration as the ILOAD changes

- Provide increased voltage regulation & balance

- Reduce temperature of cables, motors, panels generators and transformers caused by system voltage imbalance and harmonic currents

- Avoid generator shutdown in emergency startup

- Minimize telephone interference (TIF)

- Reduce ITHD and VTHD distortion to ≤ 5%

- No requirements to over-size neutral wires

- Avoid system resonance which can cause up to 100% over-voltage fluctuations

- Increase current capacity of breakers, cables, generators, panels and transformers

- Increase life of breakers, contactors, motors, rectifier circuits and transformers

- Reduce equipment downtime

- Harmonic reduction of all non-linear loads

- Non magnetic solution, no heavy transformers

- Provide transient suppression

- Enclosure options – Floor, Rack or Wall

# Typical Single-Phase Measurements of non-linear

# loads with an Active Harmonic Filter corrected

(The same criteria apply to Three-Phase Systems)

#### SAVINGS

## Power Factor Analysis

The overall Power Factor is improved from 0.70 to 0.97 with the usage of the Active Harmonic Filter.  The filter causes the KVA consumption to be reduced from the 1.5KVA to 1.28KVA, a 14.7% reduction.

Harmonic Current Analysis

The below harmonic energy spectrum depicts the correction that the injected signal of the Active Harmonic Filter reflects back to the power lines.  With the reduction of the harmonics, the ITHD is reduced from 99.2% to 5.0%.

Series 1000 – Single-Phase Product Specification

Series 2000 – Three-Phase Products Specification

Series 3000 – Three-Phase Products Specification

Series 4000 – Three-Phase Products Specification

Power Correction Systems

1800 S. Robertson Blvd.,  PMB 419

Los Angeles,  CA  90035 Phone: 1(310)247-4848    FAX: 1(310)273-7719

email: info@activeharmonicfilters.com

website: www.activeharmonicfilters.com